## Slide 1
Going Off Grid
Is it a good idea?
Presented by [presentor]
DD/MM/YYYY
Notes: “Hello everyone, and thanks for being here. Today we’re going to tackle a topic that inspires a lot of curiosity and… occasionally, confusion: going off grid. Some people picture a cozy cabin with solar panels and a wood stove; others imagine ultra-modern homes with batteries and smart controls. Both images can be true—and both can be incomplete.
By the end of this session, you’ll understand exactly what ‘off grid’ means across electricity, heat, water, and wastewater; how it differs from ‘net-zero’ or ‘energy-autonomous’ claims; the technical building blocks involved; the day-to-day reality of living with your own micro-utility; and a clear decision framework: when off-grid is wise, and when a grid-connected, ultra-efficient approach is the smarter move.”
Engagement cue: “Quick show of hands: who is here because you’re seriously considering an off-grid project? Who’s more off-grid-curious than committed?”

## Slide 2
How to use this slide deck
This Slide deck is meant as a guide and easy starting point for a person that will explain the topic to an audience that isn't familiar with the topic yet.
Feel free to adapt and expand to your own need.
  The material is licensed under CC4.0 SA BY
You can find guidance text in the notes of each slide

## Slide 3
Topics
What is going off grid?
What is the difference with net zero consumption
Benefits and Drawbacks
Conclusion

## Slide 4
What is going off grid?

## Slide 5
What is going off grid
Electricity
Natural Gas
Water
Wastewater
Notes: “When we say ‘off grid,’ we mean operating independently of public utility networks. People often focus on electricity, but true off-grid can involve:
Electricity: No connection to the utility. All power is produced on-site.
Gas: No mains gas; heating/cooking via electricity, biomass, or bottled fuel.
Water: No municipal supply; you rely on rainwater harvesting, a well, or delivered water—plus filtration and disinfection.
Wastewater: No sewer connection; you use a septic system, reed bed, or composting solutions.
This is important: the more utilities you choose to ‘unplug’ from, the more systems you must design, maintain, and pay for. If you only think about panels and batteries but ignore water and wastewater, you’re planning for only half the reality.”
Audience prompt: “If you had to choose one utility to be independent from first, which would it be, and why?”
Today we will only focus on electricity

## Slide 6
What is going off grid
Electricity:
  No meter
  No physical connection to the grid
  No costs
Notes: “Off-grid electricity means there is no safety net. There’s no invisible utility stepping in at 3am during a cold snap. Practically, that implies:
You must generate all your electricity needs, every hour of the year.
Your system must survive worst-case weeks, not average days.
You carry the full burden of peak loads, seasonal swings, and equipment failures.
Your design must include redundancy and a plan for maintenance, spares, and monitoring.
Think of it as running a tiny power company for one building or community—generation, storage, controls, and customer service are all… you.”

## Slide 7
What is going off grid
Where does the energy come from?
  Solar
  Wind
  Water
  Generator
  Batteries
Notes: “Modern off-grid systems are hybrids. Common building blocks:
Solar PV for predictable daytime energy.
Small wind where the site has consistent, strong winds.
Micro-hydro if you have flowing water with enough drop—an off-grid superpower.
Battery storage to time-shift energy from when you make it to when you need it.
A backup generator—often the difference between resilience and risk during prolonged bad weather or faults.
You’re essentially designing a resource mix that matches your site’s ‘fuel’—sun, wind, water—and your lifestyle.”

## Slide 8
What is going off grid
Solar
  Easiest to install, relatively cheap source of power
  Limited production in winter when (especially in Northern Europe) consumption is highest
  Low maintenance cost
  Reliable
Notes: “Solar is usually the backbone because it’s modular, quiet, and low-maintenance. Key nuances:
Seasonality: In higher latitudes, winter production is a fraction of summer. If you size PV for summer, you’ll struggle in winter; if you size for winter, summer will be over-abundant.
Orientation & tilt: Optimize for your winter sun if off-grid reliability is priority; a steeper tilt can help winter yield and shed snow.
Shading: Even partial shading can crater output—site analysis matters.
Surface choices: Roof vs. ground-mount. Ground-mount can be optimal for tilt, cleaning, and future expansion.
Operations: Expect periodic cleaning, mechanical checks, and performance monitoring.
Thought experiment: “Sketch your winter day: short daylight, higher heating loads, more indoor activity. How much energy is truly needed between 17:00 and 08:00? That’s what your storage and generator must cover when PV is asleep.”

## Slide 9
What is going off grid
Wind
  Limited options available for individual use
  Higher maintenance costs than solar
  Production in general complementary with solar
  Can produce noise
Notes: “Wind can complement solar—often peaking when the sun doesn’t—but it’s hyper-local:
Resource quality: You need strong, consistent winds and minimal turbulence—think high, open terrain, not behind trees and roofs.
Tower height matters: Higher = steadier, stronger wind.
Maintenance: Moving parts mean more upkeep than PV.
Noise and permitting: Factor in neighbors and local rules.
Reality check: Many sites simply don’t have the wind profile to justify small wind. Assess before you invest.”

## Slide 10
What is going off grid
Water
  Limited options available for individual use
  Higher maintenance costs than solar
  Needs a stream with water and height difference nearby
Notes: “If your site has a reliable stream with enough flow and head (height drop), micro-hydro can deliver steadier energy than PV or wind—often 24/7.
Power intuition: Roughly, more flow and more height = more power.
Controls & intake: Debris management and intake design are crucial.
Seasonality: Rivers can drop in summer or freeze in winter; you still need storage and sometimes backup.
Complexity: Installation and civil works are more involved than PV, but the payoff can be extraordinary reliability.”

## Slide 11
What is going off grid
Batteries
  Cover the mismatch between production and consumption
  Covers mismatch on a daily scale, not seasonal
  Expensive
Notes: “Batteries move energy from ‘when available’ to ‘when needed.’ Key considerations:
Chemistry: Lithium iron phosphate (LFP) is popular for stability and cycle life; other chemistries exist with different trade-offs.
Usable capacity: Nameplate ≠ usable. Depth of discharge and temperature matter.
Round-trip efficiency: Some energy is lost each cycle; design with margins.
Days of autonomy: How many days can you run with poor generation? 1–3 days is common; beyond that gets heavy and expensive fast.
Temperature: Batteries dislike extremes—thermal management improves performance and lifespan.
BMS & monitoring: A good Battery Management System and clear dashboards are non-negotiable.
Rule of thumb mindset: First shrink loads, then design storage. Storage is precious; efficiency multiplies its value.”

## Slide 12
What is going off grid
Generators
  Backup of last resort
    When no solar, no wind and batteries are empty
  Expensive to run
  Not green
Notes: “Generators are the safety valve:
When they shine: Long winter storms, equipment downtime, prolonged calm-and-cloudy spells.
Fuel choices: Diesel and LPG are common; each has storage, reliability, and emissions trade-offs.
Sizing: Big enough to handle peak loads and charge batteries efficiently, but not comically oversized (inefficient at partial load).
Integration: Auto-start features, noise control, exhaust routing, and safe fuel storage matter.
Reality: If your generator runs frequently, you’re not ‘green’—you’re off-grid. That’s okay if resilience is your primary goal, but be honest about it.”

## Slide 13
What is the difference with a net zero building?

## Slide 14
What is the difference with a net zero building?
Off Grid
  Produces all the energy it needs itself
    Solar, wind, water, generator, batteries
  No grid connection
  Supplies all the power itself at all times
  Cannot provide excess energy to the grid
Net Zero
  Produces all the energy it needs itself
    Solar, wind, water, batteries
  Grid connection
  Doesn’t supply all the power itself all the time
    Grid for peak consumption
    Grid for seasonal consumption
  Provides excess energy to the grid
Notes: Off-Grid vs. Net Zero (two-column comparison) “Both off-grid and net-zero aim to produce as much energy annually as they use, but the timing and infrastructure differ:
Off-Grid: No grid. You supply all power at all times with on-site generation + storage + generator. You cannot export excess to the grid—surplus is stranded.
Net Zero (grid-connected): You still produce your annual needs with on-site renewables, but the grid covers peaks and seasons. You can export surplus on good days and import in winter or at night. The grid functions like a huge, shared ‘virtual battery.’ This is why net-zero is usually cheaper, simpler, and greener in practice for typical sites: you don’t overbuild for rare worst weeks.”

## Slide 15
What is the difference with a net zero building?
Off Grid
  Produces all the energy it needs itself
    Solar, wind, water, generator, batteries
  No grid connection
  Supplies all the power itself at all times
  Cannot provide excess energy to the grid
Net Zero
  Produces all the energy it needs itself
    Solar, wind, water, batteries
  Grid connection
  Doesn’t supply all the power itself all the time
    Grid for peak consumption
    Grid for seasonal consumption
  Provides excess energy to the grid

## Slide 16
Benefits and Downsides of Off Grid

## Slide 17
Benefits and Downsides of Off Grid
Benefits
  No costs to electricity supplier
  Not depended on energy grid
  Certainty of energy costs
Downsides
  Need for larger production capacity to cover winter energy needs
  Need for larger production capacity to cover large startup currents of certain devices
  No backup in case of device failure
  Excess (green) energy can’t be shared with the grid
Notes: Benefits
“No costs to electricity supplier: You avoid fixed grid fees, which dominate low-consumption bills.”
“Not dependent on the energy grid: Outages and price spikes affect others, not you—if your system is well designed.”
“Certainty of energy costs: After capex, your variable costs are mainly maintenance—and occasional generator fuel.”
Downsides
“Larger production capacity for winter: You size for the darkest, coldest weeks—raising upfront cost.”
“Larger capacity for startup currents: Motors and compressors need high surge power, pushing inverter/battery sizing up.”
“No backup in case of device failure: If something key breaks, there’s no utility to lean on.”
“Excess green energy can’t be shared: On good days, once batteries are full, surplus is wasted.”

## Slide 18
Conclusion

## Slide 19
Conclusion
Going off grid is possible
Going of grid is probably not greener
Going of grid is probably more expensive
  Unless:
    Initial cost of energy connection is very high
    Energy consumption is very low and fixed costs energy connection are very high
Notes: “Going off grid is possible—especially where grid connection is very expensive or slow, or where you value autonomy above all. But for most contexts, going off grid isn’t automatically greener (if the generator runs often) and is usually more expensive than a smart, efficient, grid-connected design that uses the grid for peaks and seasons. Exceptions where off-grid can shine:
Initial cost of grid connection is very high;
Energy consumption is very low and fixed grid fees dominate. Otherwise, aim for: reduce first, harvest onsite, and let the grid act as your seasonal and peak partner.”

## Slide 20
Thank you!

## Slide 21
Acknowledgements
This slide deck Energy Digitalisation for SMEs was produced by the Every1 project and is licensed CC BY-SA 4.0, unless otherwise stated.